## Slide 1: IO-Link Safety Digitalization down to smallest functional safe Sensors/Actuators/Mechatronics
"Event" "Presenter's name"
Notes: Please enter at your convenience:
Presenter's name
Date of Event
Event (meeting, workshop, etc.)
Location of Event
For any changes, be it corrections, extensions, or translations please contact:
info@io-link.com

## Slide 2: Overview
Status of IO-Link and Basics
What is OSSDe all about?
Fieldbuses and Functional Safety Communication Profiles (FSCPs)
Requirements of Customers and Manufacturers
Why a new safe communication profile?
What did we achieve?
Integration into FSCPs
Test & assessment
Development support
Notes: In order to change the footer:
Choose "view" in the menu and then "Slide Master"
In "Slide Master" view choose again "View" and then "Slide Master"
Now you are able to change the footer text
When finished, choose "Slide Master" and close "Master View" (right side)

## Slide 3: Current status
IO-Link

## Slide 4: 11,4 million IO-Link nodes by end of 2018
Notes: An up-to-date picture can be taken from the IO-Link website: www.io-link.com
1. Go to Homepage.
2. Scroll pictures horizontally until you find the nodes graph.
3. Copy and paste picture using the right mouse button.

## Slide 5: The IO-Link Story("V1.1.3")
UDP
GA
Webserver
OPC-UA
Gateway Application
Fieldbus interface
Gateway Application
Embedded controller:e.g. Drive
Standardized Master Interface (SMI)
Device
Application
Data storage
Parameter server
IO-Link
PLC/FS-PLC/OPC-UA
Fieldbus integration
IODD
Port
Engineering
Tool
Port
"Port"
Fieldbus controller
Master / FS-Master / W-Master
Dedicated Tool
Internet, IT, Browser
e.g. XML, JSON
Air interface
W-Device
Application
Pairing button
Air interface
Ethernet
Master Tool
(IODD; Firmware Update)
IEC 61131-9
IODD
IODD
IODD
IODD
IODD Finder
FS-Device
Application
IODD
Notes: Slide demonstrates major features of IO-Link within automation:
1. Master for standard functionality; wired point-to point
2. FS-Master for functional safety; wired point-to point
3. W-Master for wireless transmission; virtual ports
4. Masters support "Data Storage" for Device's parameters; exchange w/o tools
5. "IO Device Descriptions" (IODD) as mandatory part of IO-Link devices
6. Dedicated Tool required for functional safety purposes (CRC signatures across safety parameters)
7. IODDs can be acquired from central database via "IODD Finder" Tool
8. Master Tool for parameterization via IODD; diagnosis; test; firmware update (see IO-Link specification "BLOB Transfer & Firmware Update")
9. New "Standardized Master Interface" (SMI) for harmonized Master behavior
10. Various Gateway Applications to embedded, Internet, Fieldbus, and Master Tool systems
11. Gateway Applications coordinate access to Devices, FS-Devices, W-Devices
12. Core IO-Link technology is standardized within IEC 61131-9

## Slide 6: Basics
IO-Link

## Slide 7: IO-Link Topology (Point-to-Point)
Master
Device
L+ (24 V)
C/Q (Signal)
L- (0 V)
Upper level system
Port 1 (Class A)
Unshielded cable
Device
L+ (24 V)
C/Q (Signal)
L- (0 V)
Port 2 (Class A)
. . .
Maximum 20 m
Notes: Topology is point-to-point
Master port numbering from 1 to n; "0" reserved for IO-Link Safety
3 wires, unshielded cables
Maximum length is 20 m
Power supply: 24 V industry standard
No special ASIC required

## Slide 8: Port Class A and B
1
2
4
3
5
1
2
4
3
5
I/Q
Power 1 power supply
Power 1 power supply
Power 2 extra power supply
P24 (Actuator)
N24 (Actuator)
Class B Ports shall be marked unambiguously
C/Q
C/Q
Isolated from Power 1
Class A (Device)
1
2
3
4
Class B (Device)
1
2
3
4
5
M12-4
M12-5
Master
Master
Notes: Power supply and signal options:
Port Class A with Power 1 (maximum of 1000 mA @ IO-Link Safety!)
Port Class B with extra Power 2, depending on type of connector ≥ 3,5 A and wire gauges
Power 1 electrically isolated from Power 2
Port Class B shall be marked since pin layout is not compatible with Class A

## Slide 9: Class A Power Supply (Master and FS-Master)
t
50 ms
ISIRM min
ISM min
ISM
Unspecified
behavior
Master can provide higher currents
Minimum current of the Master port
400 mA
200 mA
1000 mA (current limit for IO-Link Safety)
Notes: Master class A power supply
Shall provide a certain charge within the first 50 ms to enable wake-up procedure of the Device afterwards
Shall provide a minimum of 200 mA after initial charge time
Master can provide higher currents
At least one FS-Master port provides a maximum of 1000 mA
Derating rules are allowed, they shall be described in user manual
Port power supply can be switched off and on via SMI_PowerOffOn service

## Slide 10: SIO (Standard Input/output) to IO-Link communication
1
4
3
2
L-
I/Q
L+
SIO
COMx
4,8 / 38,4 / 230,4 kbit/s
C/Q
IO-Link communication
Switching signal ("SIO")
"Coded Switching"
Notes: Power and signals compliant with IEC 61131-2
Dual mode standard Devices: SIO (Standard Input Output) or IO-Link Communication (migration strategy)
SIO means traditional "switching signals"
IOL communication means "coded switching signals"
Three transmission rates: COM1 = 4,8; COM2 = 38,4; COM3 = 230,4 kbit/s
Pin layout corresponds to IEC 60947-5-2

## Slide 11: SIO to OSSDe and Functional Safety Communication
1
4
3
2
L-
I/Q
L+
IOL-OSSDe
COMx
4,8 / 38,4 / 230,4 kbit/s
C/Q
IOL-OSSDe: Equivalent signals
AIDA compatible!
IOL-OSSDe
OSSD: Output Switching Sensing Devices (Solid state outputs)
OSSDe: = OSSD with equivalent switching signals; type C, class 1 according to Position Paper CB24I (ZVEI)
IO-Link Safety communication
OFF state
OFF state
Testpulses
Notes: Same as SIO and IO-Link communication
Pin layout corresponds to AIDA position paper
Safety: Dual mode FS-Devices: OSSDe (default) or IO-Link Safety communication
"e" stands for equivalent switching redundant signals
FS-Device output sends and reads back short test pulses for error detection
IO-Link Safety uses the I/Q signal line (Pin 2) for OSSDe operation (OSSD2e)
The German Car Manufacturers Association (AIDA) requires the same pin layout as IO-Link Safety.

## Slide 12: Basic Start-up Procedure of IO-Link
Standard Input/Output
(SIO/OSSD)
Communication,
Identification
Configure,
Parameterize
Cyclic
Process Data
exchange
Fallback
Wake-up pulse
Mastercommand
Mastercommand
Power-on
STARTUP
PREOPERATE
OPERATE
Notes: Regular start-up of an IO-Link Device:
After power-on the Device goes into SIO mode, i.e. the signal on C/Q (Pin 4 ) is either "high" or "low". After a maximum of 300 ms it shall be ready for a Wake-up by the Master port the Device is connected to. Port goes either "low" or "high" for a defined time and thus creates a short current pulse to be detected by the Device.
Master ("port instance") switches to state STARTUP where it tries to communicate first with highest transmission rate COM3 and in case further down to slower rates (COM2, COM1) until success or retry. A Device response contains information on Master cycle time to be used for this Device. Master System Management takes over responsibility in this state and checks revision and Device compatibility with the help of information in Direct Parameter Page 1 using acyclic data exchange. A MasterCommand causes the Device to switch to state PREOPERATE.
In PREOPERATE, the Master can for example assign basic parameter values to the Device for configuration, check Data Storage and transfer technology parameter values into the Device in case of Device replacement. A MasterCommand causes the Device to switch to state OPERATE.
In OPERATE, the Master starts exchanging Process Data (PD) along with On-request Data (OD) such as parameter, SystemCommands, and Events for diagnosis.

## Slide 13: Upper level Systems (fieldbus & FSCPs)
IO-Link Safety
Notes: Usually, IO-Link Safety will be a companion technology to upper level safety systems such as safety fieldbuses.
The safety communications of such fieldbuses is standardized within IEC 61784-3 series as FSCPs.

## Slide 14: Functional Safety Communication Profiles (FSCP)
FSCP 12
FSCP 13
FSCP 14
FSCP 8
FSCP 18
Non-IEC
"C"
Non-IEC "A"
FSCP 6
FSCP 2
FSCP 1
FSCP 3
FSCP 17
IEC 61784-3-x: Collection of FSCPs
Notes: Usually, IO-Link Safety will be a companion technology to upper level safety systems such as safety fieldbuses.
The safety communications of such fieldbuses is standardized within IEC 61784-3 series as FSCPs.
FSCP1: FF-SIS  Foundation Fieldbus Safety Instrumented Systems
FSCP2: CIP Safety  Ethernet IP (ODVA)
FSCP3: PROFIsafe  PROFINET, PROFIBUS (PNO)
FSCP6: Interbus Safety
FSCP8: CC-Link Safety
FSCP12: Functional Safety over EtherCat (FSoE)
FSCP13: Powerlink Safety
FSCP14: EPA Safety
FSCP17: RAPInet Safety
FSCP18: SafetyNet_p
NonIEC A: AS-i Safety at Work
NonIEC C: CANopen Safety

## Slide 15: "Black Channel" Architecture of FSCPs
Fieldbus
FSCP
Application
Fieldbus
FSCP
Application
RIO-Gateway
Fieldbus
FSCP
Application
Fieldbus
FSCP
Application
"Black Channel"
"Safety Layer"
"Safety Technology"
FSCP Message
Notes: This figure demonstrates how a safety communication layer (FSCP) runs on top of the fieldbus layers.
The fieldbus layers are treated like a "black box" or "black channel". This means, the FSCPs are designed such that none of the securing mechanisms of the fieldbus are used for the securing concepts of the FSCP. They are independent and can be used not only for the fieldbus itself but for backplanes in remote I/Os as well (see "RIO-Gateway")
The safety communication layers usually extend the process safety data by an additional so-called safety code that ensures the necessary residual error rate.
Each device has its own functional safety technology (application) using the FSCP for exchanging safety data.

## Slide 16: Safety Function (Example)
&
Drive
Light Curtain
FS-DI Channel
User Program
Remote I/O
E-Stop
FS-PLC
Notes: In this example the safety data of the light curtain is just one bit as well as the safety data from the FS-DI channel to which the emergency stop button is connected via OSSD.
Both signals are sent via FSCP messages to the safety controller (FS-PLC). User program consists of a logical AND. The output of this AND is logically connected via FSCP message with the safe operation within the drive.
Safe operations within the drive are standardized in IEC 61800-5-2 (see slide 62). It could be - STO (Safe Torque Off  power shut down) - SOS (Safe Operating Stop  Motor position in closed loop control) - SLS (Safe Limited Speed) - etc.
Safety function is "tripped", if one of the sensors (Light curtain or E-Stop) are activated ("0"). Output of AND will be "0" also.
This corresponds to the "de-energize to trip" principle in classic relay-based safety technology (in German: "Ruhestromprinzip")

## Slide 17: Current situation with FSCPs
IO-Link Safety
Notes: Usually, IO-Link Safety will be a companion technology to upper level safety systems such as safety fieldbuses.
The safety communications of such fieldbuses is standardized within IEC 61784-3 series as FSCPs.

## Slide 18: Manufacturer's Situation
Safety controller (FS-PLC)
Remote I/O with FS modules
FS-DI
e.g. Emergency Stop
Fieldbus / FSCP
FS-PLC
Redundant signal lines
FS = functional safety
PLC = programmable logic controller
Notes: This slide shows a fieldbus arrangement focusing on typical safety components such as:
Level switches,
Laser scanners,
Light curtains,
Drives/motors,
Robots,
Programmable logic controllers including safety data processing (FS-PLC)
Remote I/O with safety modules for - Analog Input (measurement) - Analog Output (positioner) - Digital Input (Emergency Stops) - Digital Output (Relay)
These components are using an FSCP for communication of safety data since a normal fieldbus cannot guarantee the required residual error rate for safety data transmission required by safety standards such as IEC 61508.
IO-Link Safety focuses on the typically redundant connections between Remote I/O safety modules and the final sensors and actuators. There are many different connection technologies with de-facto standards such as OSSD.

## Slide 19: Customer's Situation
Machine builder decides on type of fieldbus to be used depending on deployment case
Thus, specific devices for each fieldbus with separate spares inventory, version maintenance and service are required
Thus, high degree of persistence to stay with "classic" interfaces such as OSSD, 4 to 20 mA, and etc. on "remote IO" field devices, since they are independent from fieldbus
However: no connection to Internet-of-Things (IoT) and Industry 4.0
Numerous new applications: (see "Smart Manufacturing") - New sensor technologies, e.g. strain, torque, pressure, multi-sensing, and etc. - More measuring sensors, e.g. object types, distance - Mechatronics, e.g. combinations sensors/actuators
Progressive miniaturization
Notes: No connection to Internet-of-Things (IoT) and Industry 4.0 means all the benefits of IO-Link and IO-Link Safety:
Connectors and wiring same as IO-Link. Power supply same as IO-Link. However, limited to 1000 mA with port Class A.
IO-Link Safety standardized an OSSDe (solid state outputs, equivalent switching redundant signals, specified test pulses)
Off-site parameterization and test also for safety devices that are intended for use on FS-DI modules within Remote I/Os.
IO-Link Safety communication is suitable for safety functions up to PLe or SIL3 respectively.
IO-Link Safety concept approved not only for cyclic safety communication protocol but for the entire parameterization and verification including functional safety Master Tools via Standardized Master Interface (SMI).
Device replacement not only for standard IO-Link but for FS-Devices also ("Data Storage").
Manufacturer can focus on one FS-Device for the entire world market.

## Slide 20: IO-Link Safety as a Solution
Remote I/O
0
7
0
7
0
7
Fieldbus with one of the FSCPs (IEC 61784-3)
0
7
0
7
DI
FS-Master
AI
OSSDe
or
COM
Switches
Analog
measure-
ments
Digitized
measure-
ments
Intelligent
drives
0
7
DO
Relays
0
7
AO
OSSD
e.g. 0 to 10 V
PM switching
IO-Link Safety
Notes: Refer to slide 18 (remote I/O)
Effect here is the same as with standard IO-Link. Instead of several different modules within a remote I/O such as FS-DI, FS-DO, FS-AI, and FS-AO, the user can focus on one FS-Master and save space, invest, and spares inventory .
Long lasting discussions for product managers about the number of channels in modules can be alleviated.
Various different module interface technologies (OSSD, 0 to 10 V, 4 to 20 mA, etc.) become more and more obsolete.

## Slide 21: Automation "hierarchy" with IO-Link Safety
Higher-Level Systems
Enabling New Markets
IO-Link Devices
a Worldwide Standard
PLC Level
Fieldbus Level
with IO-Link FS-Master
Sensor / Actuator /
Mechatronic Level
with IO-Link Safety
(Functional Safety)
Devices
SIO Mode
safety
safety
FS-Devices
OSSDe Mode
(mapping and/or local processing)
Valves | Locking Units | Light Curtains
Notes: This figure shows how IO-Link Safety fits into the automation hierarchy with IO-Link. It is integrated and not separated in this pyramid.
It is assumed that PLCs provide features for safety data processing, so-called Safety PLCs, for example according IEC 61131-6. They receive safety data from functional safe sensing devices and send safety data to functional safe actuating devices.
On fieldbus level, IO-Link expands its product range now by Safety Masters (so-called FS-Master) that can play the role of a standard non-safety Master as well. That means, the following Devices can be connected:
Safety sensors (so-called sensing FS-Devices)
Safety actuators (so-called actuating FS-Devices)
Mixed safety devices (so-called mechatronic FS-Devices)
Safety sensors via OSSD (redundant switching signals)
Standard non-safety Devices
It is possible to enhance an FS-Master such that it is able to process safety signals and thus allow for local sub-"safety functions".

## Slide 22: "Off-Site" Parameterization and Test (OSSDe)
FS-Device
"USB Master" Tool software
with safety
Parameter
Remote IO
0
7
0
7
0
7
0
7
FS-Device
F-DI Modul
FS-Master
Fieldbus
OSSDe
Test
Off-site configuration & parameterization
USB
"USB-Master"
History
IODD
Notes: Off-site means away from the machine or facility, for example in the office or "en route".
On-site means connected to the automation system of a machine or facility including IO-Link for commissioning, change or maintenance reasons.
Off-site configuration, parameterization and testing:
FS-Devices with standardized OSSDe can be connected to USB-Master for parameterization and test.
Parameterized FS-Device can be connected to FS-Digital Input module (remote I/O).
FS-Devices can be connected to USB-Master for parameterization and testing while in IO-Link Safety communication mode, if USB-Master supports this mode.
In the past, usually many different adapter cables between parameterization tools and safety devices have been necessary. (history).

## Slide 23: Migration Strategy (example: PROFIsafe)
Fieldbus (FSCP)
IO Level ("OSSD")
F-DI
F-Sensor
F-Device
IEC 61784-3-3
FS-Master
FS-Device
F-DI
Remote IO
FS-Master
Remote IO
Connect… (Subset)
Connect…
and others…
PROFIsafe 1999
IO-Link Safety 2018
ZVEI CB24I
Develop…
Develop…
Connect…
New: OSSD + communication
OSSD
Notes: From a safety sensor's point of view:
With the advent of FSCPs, the safety device manufacturer had the choice between - connecting his device to an F-DI module in a Remote I/O provided by the safety PLC manufacturer, or - developing a variant with FSCP communication capabilities.
Now with the advent of IO-Link Safety, the safety device manufacturer can develop one new version with OSSDe and IO-Link Safety communication that can be connected worldwide to - F-DI modules as before, or - IO-Link Safety FS-Masters
There is no standardization for general OSSD and many different implementations make applications more difficult: F-DI modules require adjustable filters against test pulse and signal discrepancy effects. IO-Link Safety chose type C, class 1 parameter sets from the CB24I position paper (ZVEI) for OSSDe and thus created a standard.

## Slide 24: Communication
IO-Link Safety
Notes: What is IO-Link Safety communication all about?

## Slide 25: Specifications and Assessment Reports
Notes: First specification published in April 2017. This version contained already everything to start implementation of the OSSDe, protocol and parameterization parts.
Version 1.1 with SMI was published in April 2018. This version contains now the new "Standardized Master Interface" developed by the IO-Link Community (Coreteam) as basic technology for all new Masters. SMI is essential for IO-Link Safety since it allows for a complete assessment of the entire safety concepts of IO-Link Safety. Without SMI, this part of the assessment would have been on implementation (each designer/manufacturer) and not on concept level (working group only).
See slides 51 to 56 for details on SMI
See slide 59 to 61 for details on assessments
Besides IO-Link Safety System Extensions, the following documents have been developed:
Several documents for the safety assessment by assessment bodies
IO-Link Safety – Test & Assessment with the automatically created test scripts for FS-Device and FS-Master Testers
White Paper for Integration of IO-Link Safety into FSCPs
Concept approval by TÜV-SÜD
Concept approval by IFA (German Berufsgenossenschaften)

## Slide 26: "Black Channel" Principle also with IO-Link Safety
Master (Stack)
IO-Link Safety
IO-Link Safety
Device (Stack)
Standard
application,
e.g. Diagnosis
Safety application
Safety Communication Layer (SCL)
IO-Link ("Black Channel")
Safety application
Standard
application,
e.g. Diagnosis
FSCP (e.g. PROFIsafe)
Gateway
Point-to-point communication
Notes: This figure illustrates IO-Link Master and Device stacks as "black channel" for the safety communication layers (SCL) of IO-Link Safety.
Safety measures of IO-Link Safety do not take any benefits from the error detection mechanisms of the "black channel".
On FS-Device's side, the safety application corresponds to the firmware of the safety technology such as light curtain, laser scanner, strain, pressure or temperature transmitters, etc.
On FS-Master's side, the safety application is usually a gateway to an FSCP (safety PLC) or embedded safety system.

## Slide 27: Messages with IO-Link Safety
Safety
Process Data Out
Control
&
M-Counter
CRC
Signature
3/25 octets
1 octet
2/4 octets
Safety
Process
Data
In
Status
&
D-Counter
CRC
Signature
3/25 octets
1 octet
2/4 octets
32 to 0 octets
Non-safety Process Data Out
Port number
1 octet
Port Number
1 octet
From FS-Master:
From FS-Device:
32 to 0 octets
Non-safety
Process
Data
In
Notes: Top figure demontrates an IO-Link Safety message from the FS-Master to the FS-Device. It starts with the output safety data, followed by the port number of the FS-Master, followed by a control byte including a 3-bit counter value, followed by a CRC signature across all yellow marked parts. Non-safety process data can be attached at the end. Their length depends on the length of the yellow part.
Two protocol modes are possible:
Short process data 0 to 3 octets with a CRC signature of 2 octets (optimized for fast operation)
Longer process data 0 to 25 octets with a CRC signature of 4 octets
The IO-Link Safety message from FS-Device to FS-Master corresponds to the message from the FS-Master except for:
Counter value is inverted
Port number is taken from a stored value during commissioning and inverted also.
Permitted data types are Boolean, Integer16, Integer32, Qualifier
Important to know is that IO-Link Safety uses explicitly transmitted safety codes (see IEC 61784-3).
Qualifier bits are used during mapping of safety data to FSCP layer.

## Slide 28: Start-up and Securing Measures
SIO / OSSDe
Communication,
Identification
Configure,
Parameterize
Cyclic
Process Data
exchange
PowerOffOn
Selftest
Mastercommand
Mastercommand
Ready
Wake-up
PowerOffOn
Safety parameter verification (VerifyRecord)
Misconnection? (Authenticity/Port check)
Replacement? (Data Storage if "out-of-the-box")
Parameter verified?
 Start safety communication (SCL)
Notes: Regular start-up of an FS-Device:
After power-on the FS-Device goes into SIO mode, i.e. the signal on C/Q (Pin 4 ) is either "high" or "low". After safety self-tests, the FS-Device sends a "READY" pulse on C/Q, whereupon the FS-Master initiates IO-Link commun ication via a Wake-up pulse to the FS-Device: signal on C/Q goes either "low" or "high" for a defined time and thus creates a short current pulse to be detected by the FS-Device to start communication.
FS-Master ("port instance") switches to next state (STARTUP), where it negotiates the correct COM transmission rate until success or retry. An FS-Device response contains information on Master cycle time to be used for this Device. FS-Master System Management checks revision and FS-Device compatibility. A MasterCommand causes the FS-Device to switch to next state (PREOPERATE).
In this state, the FS-Master sends a so-called "VerifyRecord" with safety protocol parameters to the FS-Device to ensure correct parameterization of the FS-Device. In case of misconnected FS-Devices to either a wrong FS-Master or Port, the FS-Master detects incorrect authenticity parameter values creates an error message and blocks safety communications. In case of an FS-Device with "Out-of-the-Box" parameterization (= factory settings), the FS-Master activates the IO-Link Data Storage mechanism and transfers safety technology parameter values into the FS-Device (FS-Device replacement without tools). A MasterCommand causes the FS-Device to switch to the next state (OPERATE).
In this state, the FS-Master starts safety communication (SCL) if all safety parameters have been correct at evaluation.

## Slide 29: Integration into FSCPs
IO-Link Safety
Notes: What is IO-Link Safety communication all about?

## Slide 30: Integration Objectives of IO-Link Safety
FSCP 3
Ethernet-based
"Classic fieldbus"
FSCP 2
Ethernet-based
"Classic fieldbus"
FSCP 12
Ethernet-based
FSCP 8
Ethernet-based
"Classic fieldbus"
RIO
FS-DI
FS-DI
RIO
FS-DI
RIO
FS-DI
RIO
Switches, OSSD,
OSSDe
"One" safety device with OSSDe and
IO-Link Safety communication
FS-Device
FS-Master 3
FS-Master 2
FS-Master 12
FS-Master 8
RIO = Remote I/O
Notes: For FS-Devices:
Dual mode operation:
OSSD, when connected to an FS-Digital Input module, or
IO-Link Safety communication, when connected to an FS-Master
For FS-Masters:
Usually, FS-Masters for the different fieldbuses/FSCPs can be realized as an FSCP node using existing FSCP development kits. The safety layers of the FSCP and of IO-Link Safety can be combined and encapsulated to achieve reasonable efforts for IO-Link Master manufacturers (see slides 53 and 54).
At least one FS-Master per FSCP is required for FS-Device manufacturers to enter into that particular market.

## Slide 31: Prospects
FSCP A
Ethernet-based
"Classic"
FSCP B
Ethernet-based
"Classic"
FSCP C
Ethernet-based
FSCP D
Ethernet-based
"Classic"
FS-DI
RIO
IOL-S
FS-DI
RIO
IOL-S
FS-DI
RIO
IOL-S
FS-DI
RIO
IOL-S
Dual mode FS-Device (OSSDe)
Largest commonality for sensors, actuators, and
mechatronics



Local signal processing
Port Class B

FS-Device
Notes: As explained in previous slide, FS-Devices benefit from the largest commonality for safety sensors, actuators and mechatronics due to bi-directional communication of IO-Link Safety on any FS-Master.
Dual mode FS-Devices with standardized OSSDe allow for operation on classic FS-DI (digital input) modules within remote I/Os and with IO-Link Safety communication on FS-Master ports. FS-Master ports with OSSDe capability allow for operation of dual mode FS-Devices or classic OSSD sensors according Type C of "ZVEI Position Paper CB24I" (see slide 28 and 30). This flexibility allows the customer to start with a classic OSSD sensor type in his application until a new version (FS-Device) will be available.
The encapsulation of the safety communication layers within an FS-Master allows for an extended mapping of the safety data including a safety logic processing unit. With the help of this unit local safety functions can be build using sensor and actuator FS-Devices connected to this particular FS-Master.
FS-Devices requiring more than 1000 mA (mostly actuators) can use FS-Masters providing port class B with extra Power supply 2 (see slide 6).

## Slide 32: Integration
In progress:
PROFINET / PROFIsafe
PROFINET Integration
White Paper
Role model for
Fieldbus / FSCP
White Paper
Available on:
www.io-link.com
Notes: One of the standard IO-Link integration documents covers mapping of IO-Link to PROFINET. This document is comprehensive and can serve as a role model for integrations.
A White Paper with concepts for integration concepts to PROFIsafe is available also and provided on the IO-Link websites in a neutralized form for download .

## Slide 33: System Overview (PROFINET / IO-Link)
IO controller
Engineering System
IO-Link PDCT
IODD (Device, FS-Device)
IO supervisor
PROFINET/PROFIsafe
PROFINET domain
IO-Link domain
GSD (IO device)
Off-site commissioning
PNIO
IO- Link
IO- Link
Linking Module (B) "safety"
FS-Devices/Devices
IO device
Port 1
Port 2
Port 3
Port 4
FS-Master
Notes: This overview shows exemplary via PROFINET/PROFIsafe, how a so-called Linking Module provides the gateway with the mapping of safety Process Data.

## Slide 34: Safety is Linear Extension of Fieldbus Integration (Example PN)
PROFINET
Gateway: PROFINET IO-Link Integration ("Linking Modules")
PROFIsafe
Standardized Master Interface (SMI)
Configuration Manager
(Parameter) Data Storage
Acyclic Data Exchange
Diagnosis Unit
FS-IO mapping
IO-Link Safety (COM)
FS-DI (OSSDe)
Splitter/Composer
Cyclic Process Data Exchange
Master layers
PROFIsafe services + Protocol state machine
IO-Link Safety services + Protocol state machine
PROFIsafe ‒ IO-Link Safety Gateway
FS-Device
PROFIsafe
IO-Link Safety
PROFIsafe development kit
Notes: Safety integration is a linear extension of the fieldbus integration. Usually, there exist development kits for particular FSCPs such as PROFIsafe.
In case of SIL3 applications, these development kits recommend redundant microcontrollers to carry the FSCP protocol firmware.
IO-Link Safety fits well into this approach since it can be implemented totally hardware independent.
This figure shows also the "black channel" character of the FS-Master. The core part is a standard non-safety IO-Link Master with two modifications:
An FS-Master Port is able to sense the "READY" pulse of an FS-Device
An FS-Master is able to split the SPDU (safety protocol data unit) from the entire IO-Link message. In contrast, an FS-Master is able to compose an entire IO-Link message out of an SPDU and a non-safety data part.

## Slide 35: Test & Certification
IO-Link Safety
Notes: Which kind of testers are available?
What kind of assessment and certification rules exist?

## Slide 36: Test & Assessment
Step 1 is achieved: Draft V1.0 with SCL + OSSDe
Step 2 Draft V1.1 comprises the complete tests
Content:
OSSDe
FS-Device functions
FS-Master functions
SCL tests (automated test script generation)
FS-Master Tool tests
Assessment & certification
SCL = Safety Communication Layer
Notes: Content:
Physical layer tests (OSSDe)
IODD checks
Configuration test for FS-Devices
Safety communication test scripts for FS-Devices (automatically created)
Verification tests for FS-Devices (VerifyRecord)
Reference test for FS-Devices (entire integration)
FS-Master protocol test
Safety communication test scripts for FS-Masters (automatically created)
Reference test for FS-Masters (entire integration)
Environmental tests
Annex A: Testing principles
Annex B: Assessment
Annex C: Conformity
Annex D: Manufacturer declaration

## Slide 37: Automated Test Case Generation
IO-Link Tester
Sequence charts
Test scripts
Notes: The test patterns for the safety communication layer tester for FS-Device and FS-Master have been created automatically during simulation of the FS-Master and FS-Device state machines.
Modeling of the protocol state machines was done using Unified Modeling Language technology.
Model checking was performed to find systematic design errors such as dead-locks and etc.
Simulation was performed using the UML model to find out resilience of the model against errors or failures . Several use cases lead to corresponding sequence charts.
Last but not least, a test case generator was used to create automatically test cases with a test coverage of 100% applying Modified Condition/Decision Coverage approach. This way many redundant test cases could be sorted out in order to create a set of relevant test cases.

## Slide 38: FS-Master Tester
Fieldbus- Interface
FS-Master (EUT)
FS-Master- Tester-HW
e.g. USB
IO-Link
Fieldbus
Initialize FS-Master, and Activate test mode, and PowerOFF/ON
FSCP
Test-
FW
SPDU
Message
SPDU
Non safety part used as "test control channel" to "UT"
IOL-Safety
Mapper
UT
SMI
Notes: The FS-Master Tester consists of the following parts and subparts:
The test program runs in a laptop and uses the test scripts we have seen within the last slide.
Via USB it is connected to the special "FS-Master Tester Hardware" playing the role of an "FS-Device" to the FS-Master (equipment under test).
The special "FS-Master Tester Hardware" receives the test scripts and stimulates the IO-Link Safety communication test case by test case.
This way IO-Link messages with an SPDU arrive at the FS-Master's IOL-Safety layer and the Mapper to the upper-level-system "FSCP".
The non-safety part of the messages is used as a means to mirror back the received signals and data to the "FS-Master Tester Hardware" and finally to the test program in the laptop for evaluation.
The next slide illustrates how this signal and data mirror works.

## Slide 39: FS-Master Tester (without fieldbus dependency)
Fieldbus layers / Ethernet
Gateway IO-Link/PROFINET
FSCP
Standardized Master Interface (SMI)
FS mapping
IO-Link Safety
FSCP Test
IO-Link safety Test
Master layers
FS-Master Tester
FS-Master
Temporary test signal channel (part of the safety implementation)
SPDU
Test signal data
Notes: The mapping unit contains a so-called Upper Tester layer, which mirrors signals and data between the safety and the non-safety channels ("temporary test signal channel"). This blue colored part can be switched on via safety protocol parameters for protocol testing purposes.
This approach allows for a simple and efficient protocol testing (FS-Master Tester) independent from a particular FSCP.

## Slide 40: FS-Device Tester
FS-Device- Tester
e.g. USB
IO-Link
FS-Device (EUT)
Notes: Extension of standard non-safety Device tester. Test scripts can be configured to adapt to the process data of the FS-Device defined in its IODD.

## Slide 41: Assessment & Certification (FS-Device or stand-alone FS-Master)
IO-Link partner starts developing an FS-Device or stand-alone FS-Master
EMC test
Electrical safety check
IO-Link VendorID
Basic IO-Link Device test ("black channel")
Safety assessment by Assessment Body
Optionally: Role of the Test Center
Test of FS-Device (SCL + opt. OSSDe) "Test standard"
not passed
IO-Link manufacturer declaration
Including certificate number
Certificate from Assessment Body
Test and check successfully passed
+
Immunity (EMC) + E-safety
Interoperability (IO-Link)
Conformance (IEC 61508)
Availability, immunity and electrical safety (IO-Link)
Functional Safety
Corrections
passed
Assessment successfully passed
Test Center (fulfills Testlab instructions):
Test of FS-Device (SCL + optionally OSSDe)
"Reference standard"
Notes: Test, assessment, and certification of FS-Devices comprise three aspects: - Conformity with regulations, for example European directives (EMC for functional safety such as IEC 61000-6-7 and electrical safety such as IEC 61010-2-201) or Underwriters Laboratories – UL (UL508 – "Class 2", single fault prove) - IO-Link Interoperability (conformity of the FS-Device with the IO-Link specifications: The IO-Link community arranged for "Test standards" based on the Test & Assessment specification and supported by Technology Providers) - Conformance of functional safety development process with IEC 61508 (due to software/firmware involvement)
While developers can use the IO-Link "Test Standards" during development to ensure a high degree of conformity/interoperability with IO-Link and IO-Link Safety, this is not enough for functional safety. IO-Link Safety requires particular Test Centers assessed by the IO-Link Community and an Assessment Body and audited periodically. These Test Centers are performing tests and checks according to approved "Test Lab Instructions" and using approved "Reference Standards". "Test Standards" and "Reference Standards" correspond to each other. However, while the "Test Standards" can be variable to a certain extent, the "Reference Tests" are fixed and "locked" by CRC signature.
A safety assessment body can play the role of a Test Center on behalf of the IO-Link Community, thus reducing time and effort.
After the final certificate of the Assessment Body, the FS-Device manufacturer can issue the IO-Link Safety Manufacturer declaration showing the certificate number of the assessment.

## Slide 42: Assessment & Certification (FS-Master on Fieldbus/FSCP)
IO-Link partner starts developing an FS-Master
EMC test
Electrical safety check
Prove Fieldbus and FSCP conformity
IO-Link VendorID
Basic IO-Link Master test ("black channel")
Safety assessment by Assessment Body
Optionally: Role of the Test Center
Test of FS-Master (SCL + opt. OSSDe) "Test standard"
not passed
IO-Link manufacturer declaration
Including certificate number
Certificate from Assessment Body
Test and check successfully passed
+
Immunity (EMC) + E-safety
Interoperability (Fieldbus and IO-Link)
Conformance (IEC 61508)
Availability, immunity and electrical safety (Fieldbus and IO-Link)
Functional Safety
Corrections
passed
Assessment successfully passed
Test Center (fulfills Testlab instructions):
Test of FS-Master (SCL + optionally OSSDe)
"Reference standard"
Notes: Assessment and certification of FS-Masters on fieldbus/FSCP follows a similar concept:
EMC tests and electrical safety issues can be different depending on the standards to be considered (generic, domain, or product)
Usually, from a fieldbus/FSCP point-of-view, the FS-Master is a fieldbus device and has to be developed, tested, and assessed according to the interoperability/conformity rules of the particular fieldbus/FSCP. The result is a certificate of the fieldbus organization.
The remaining steps correspond to those of an FS-Device.

## Slide 43: Development SUPPORT
IO-Link Safety
Notes: How can I get help with my development?

## Slide 44: Technology Provider
"Development Support"
  "Functional" versions for FS-Device and FS-Masters are already available (no SIL).
  Developers can implement without waiting on an "official" counterpart of the market
"Starterkits"
  "Functional safety" versions will show up
  Safety development with support from assessment bodies
  Pre-certified "SCL-driver" software for up to SIL3/PLe, assessed on one HW,
  Architecture, design, and testing according IEC 61508/ISO 13849,
  Implementation µC independent (ANSI-C?) and according MISRA (2012) standard,
  Product and marketing strategy depending on technology provider
FS-Master
FS-Device Dev.
FS-Master Dev.
FS-Device
Cert. Driver
FS-Master + Tool

## Slide 45: What's next?
Finalization of the Test Specification in fall 2019 (Draft for WG-Review; dependancy on V1.1.3 test
FS-Master and FS-Device-Tester in 3rd quarter of 2019
"White Paper" to be incorporated in Integration Specification PROFINET/PROFIsafe Ed. 2
Encourage and enable other FSCP integrations (FSoE, CIP-Safety, and etc.)
IO-Link Safety workshop on 9th and 10th of October 2019
Certified designer training classes starting in spring 2020
Investigations on IO-Link Safety protocol extensions for IO-Link wireless (HS University, Hamburg)

## Slide 46: Working Group Members

## Slide 47: Thank you!
See you @